## Slide 1: Parametric Model Design for 3D Printing
David Spencer Tyree david.tyree@ca.com
CA Maker Group

## Slide 2: An introduction to OpenSCAD
Type here
See it here

## Slide 3: OpenSCAD is amazing! (These are random things from thingiverse)

## Slide 4: Diving in!
www.openscad.org
  It’s free!
  It works on every major platform
  Produces dimensionally accurate designs (by default all units are MM)
To use it for 3D Printing
  Type in your design
  Render it
  Save it to a .STL file
  Use a Slicer to convert the .STL file to a .GCODE File
  Print!

## Slide 5: Shapes
You type in the shape’s you want
  cube[x-dimension,y-dimension,z-dimension]);
  cylinder(r=radius,h=height)
  sphere(r=radius)
You can modify the shapes by adding:
  center=true - center the shape
  $fn=fineness – adjust the fineness of the generated shape
  etc

## Slide 6: Modifying Shapes
You can modify a shape using these commands
  translate([moveByX,moveByY,moveByZ])
  scale(newScale) or scale([scaleX,scaleY,scaleZ])
  rotate([rotateX,rotateY,rotateZ])
Modify a shape by placing the command before it or by putting the shapes in braces ‘{}’

## Slide 7: How to select what to modify
Modify a single shape
  rotate([45,0,0]) translate([1,0,0]) cube([1,1,1]);
    You can chain modifications
    The order matters! (move then rotate != rotate then move)
      First translate (move)
      Then rotate
Modify a collection of stuff
    rotate([45,0,0]) translate([1,0,0]) {
      cube(1,1,1);
      scale(1.5) sphere(r=2);
    }
Operations are applied in reverse order
  sphere(r=2) is first scaled, then translated and finally rotated

## Slide 8: Union
  union(){ }
    Produce a shape by combining all the shapes

## Slide 9: Difference
You can perform operations on shapes to create new shapes
  difference(){ shapeA(); shapeB(); shapeC(); }
    Subtract shapes from each other
    shapeA-(shapeB+shapeC)

## Slide 10: Intersection
  intersection(){ }
    Product a new shape from the intersection of shapes

## Slide 11: Hull
  hull(){ }
    Produce a shape by combining the profiles of two shapes

## Slide 12: Minkowski
  minkowski(){ }
    Produce a shape by tracing one shape around another
      This will trace the cylinder around the cube

## Slide 13: Rotate & Extrude
  rotate_extrude(){ }
    Produce a shape rotate it and extruding it

## Slide 14: Modules
  Modules let you combine a bunch of shapes and operations into a single thing so you can re-use.
    They also let OpenSCAD cache a shape

## Slide 15: Composite shapes!

## Slide 16: Loop & Iterate
  OpenSCAD has variables
    i=5; //set I to 5
  You can loop or iterate with openscad
    for(variable=[start:increment:end){
    }

## Slide 17: 3D IO The power is in combinations
Inputs
  3D Model (.OBJ, .STL)
    Thingiverse, Sculptris, Wings3D, 123D Catch, etc
  2D Models / Drawings (.DXF, .SVG, PD)
    Inkscape, Autocad, QCAD, Desktop Scanner, etc
OpenSCAD can import and use these files
  import(“kitten.obj”);
You can then use them like any other shape!

## Slide 18: Importing things!

## Slide 19: Using libraries
OpenSCAD has a large number of libraries
  MCAD ( https://github.com/elmom/MCAD )
    Screws, gears, servos, steppers, motors, bolts, etc
  Thingiverse
Download the library and then import it
  Usually the library will have instructions inside of how to use it

## Slide 20: Designing stuff!
What requirements?
What tools / inputs do I have ?
  Capture from real life
    Desktop Scanner / 123D Catch
  Model it
    Sculptris, Thingiverse, Sketchup
Can I print it?
  Does it have big overhangs?
  How dense does it need to be?
  How accurately must it be printed to work (0.3mm is what I consider the minimum feature size to be useful)

## Slide 21: Slicing
After creating the thing we choose some print settings

## Slide 22: Slicing
After designing the model it is time to print it! (I use Slic3r)
  Choose a density and fill pattern
  Choose number of top / bottom layers
  Choose number of perimeter
Print the generated .GCODE file (I use Printrun)

## Slide 23: Example: Quick disconnect for cool suit for racing (Drawing it out on paper is a must for this one)
A hose connector for quickly disconnecting hoses for a cool suit, which can be mounted on the side of a cooler
  Must disconnect quickly and easily
  Must plug back in easily
  Must not let it pump water out of the cooler
  Must be printable

## Slide 24: Example: A custom JIG for drilling out a snapped bolt on a motor
You want to build a JIG to drill out a snapped exhaust bolt.
  Use a desktop scanner to scan a new gasket for the exhaust
  Convert the scanned image to a .SVG/.DXF file
  Extrude it with OpenSCAD

## Slide 25: Example: A Fallout PitBoy
You want to build a Fallout Pitboy
  You can use 123D catch to acquire a model of your wrist
  You can then use a 3D model of the PitBoy and subtract the model of your wrist from it.